## Slide 1: Efficient Utilization of GPGPU Cache Hierarchy
Mahmoud Khairy, Cairo University, Egypt
Mohamed Zahran, New York University, US
Amr G. Wassal, Cairo University, Egypt

## Slide 2: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 3: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 4: GPGPU is a Hot Topic of Research
Chart: 
| 2007-2009 | 2010 | 2011 | 2012 | 2013 | 2014
Series 1 | 4 | 6 | 9 | 11 | 27 | 29
Number of research papers related to GPGPU published in the last 7 years at the
top-tier computer architecture conferences (MICRO, ISCA, ASPLOS, HPCA)
15 % of papers
# papers
Research focuses on:
1- High performance GPGPUs (memory, caches, control divergence, ..)
2- GPGPU programmability (Coherence, Consistency, Transactional Memory,…)
3- Power-Efficiency
4- Improving CPU-GPU integration
5- Fault-Tolerance

## Slide 5: Why GPU caches?
Modern GPUs are equipped with general purpose on-chip cache hierarchy in order to:
  Reduce on-chip memory bandwidth demand
  Increase memory system throughput
  Improve the performance of some irregular GPGPU applications
  Enhance the GPGPU programmability
However, due to the massive multithreading, GPGPU caches suffer from severe resource contention and low data-sharing which may degrade the performance instead.

## Slide 6: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 7: Cache Thrashing
GPU caches are not designed to keep the per-thread working set.
GPU caches were designed to exploit some access patterns that exhibit small cache footprint per warp and can fit in the cache (e.g. Coalesced accesses).
In case, GPGPU applications rely on caches to exploit data locality and they contain a large cache footprint per-thread, the active threads will compete on the few available cache lines and the L1 cache will be vulnerable to thrashing.
Source: Minsoo Rhu, “A Locality-Aware Memory Hierarchy for Energy-Efficient GPU Architectures “, MICRO 2013
 | Intel Core I7 | IBM Power7 | NVIDIA Fermi | NVIDIA Kepler
L1 cache size | 32 KB | 32 KB | 16-48 KB | 48 KB
Threads/core | 2 | 4 | 1536 | 2048
L1 / thread | 16 KB /thread | 8 KB /thread | 10-32 B / thread | 24 B /thread

## Slide 8: Conflict Contention
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Memory-coalescing
Warp Threads’ memory loads
Indexer
L1 Cache

## Slide 9: Conflict Contention
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Memory-coalescing
Indexer
causing severe stalls and conflict misses
Two Types of Conflicts:
  1- Intra-Warp Conflict Contention: Threads within the same warp
  2- Inter-Warp Conflict Contention: A group of coalesced warps
L1 Cache

## Slide 10: Sequential Interleaving Indexer
Conflict Degree n=M/gcd(M,S)
  M number of cache sets
  S is the stride of sequence
For example, assume a reference stream with an access stride of 2 (i.e. 0,2,4,6,8,10,12,14) has a 4-way conflict degree (i.e. mapped to only 4 cache sets out of 8)
Even strides will cause a high level of conflict degree, while odd strides don’t cause any conflicts (recall that M is a power-of-2 number).
The worst case scenario occurs when the reference sequence has a stride which is a multiple of M, thus causing a 1-way conflict.

## Slide 11: 1-way Conflict Contention Example
When K is multiple of the number cache sets, all 32 threads will map to the same cache set.
//from SYRK
//element c(i,j) = row i*row j
int j = blockIdx.x * blockDim.x + threadIdx.x;
int i = blockIdx.y * blockDim.y + threadIdx.y;
int k;
for(k=0; k< M; k++)
{
c[i * N + j] += alpha * a[i * M + k] * a[j * M + k];
}
K * cache line
A Matrix
Thread 0
Thread 1
Thread 2
Thread 31
.
.
.

## Slide 12: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 13: Experimental Setup
GPGPU-sim 3.1.2
  Nvidia GTX 480 (15 Fermi cores)
Main Benchmarks :
  Rodinia (8 Apps)
  CUDA SDK (6 Apps)
  PolyBench (4 Apps)
Notes: Add the L1/L2 write policy

## Slide 14: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 15: Cache Sensitivity
Chart: Normalized IPC
| BLK | Sprod | VAdd | FWT | NW | HS | CONV | SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV | PEst | B+tree | BP | NN
Bypassing | 1.0694 | 1.371 | 1.7768 | 1.0081 | 1.4787 | 1.4904 | 1.9078 | 2.9934 | 1.0687 | 0.83852 | 0.80225 | 1.0034 | 0.37518 | 1.3455 | 0.98018 | 1.5167 | 2.5746 | 1.9758 | 0.5041 | 0.41114 | 0.56121 | 0.16358
Bounded (16KBL1+786KBL2) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Unbounded | 0.99187 | 1.0191 | 1.0043 | 1.3049 | 1.7436 | 1.4948 | 1.5374 | 2.919 | 1.2892 | 2.905 | 3.1817 | 5.6892 | 3.0562 | 3.9329 | 6.0089 | 7.191 | 37.4666 | 38.9254 | 1.5557 | 1.1099 | 1.0676 | 1.0712
Bypassing better than Bounded
and Unbounded
Unbounded and Bypassing better than Bounded
Unbounded is better by an order of magnitude
Bounded is better than bypassing
Notes: Bypassing means totally bypassing L1/L2 caches (i.e. no caches)
Unbounded was emulated by 256 sets 64-way L1 cache (2 MB) (almost only cold misses occur)

## Slide 16: L1/L2 Data Locality Analysis (Read only)
Chart: 
IntraWarp | 0 | 0 | 0 | 0 | 3.7085 | 0 | 130.423 | 61.3103 | 0 | 820.902 | 2118.18 | 6.6045 | 784.412 | 1347.49 | 1877.18 | 1886.66 | 367.182 | 243 | 4077.18 | 254.524 | 959.705 | 5413.97
IntraBlock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 53.1827 | 598.048 | 714.498 | 956.599 | 146.74 | 416.129 | 0.59148 | 0.030643 | 1.7783 | 8.3801 | 2 | 0 | 243.323 | 1515.11 | 3.578
IntraCore | 0 | 0 | 0 | 0 | 0.0024899 | 23.3434 | 12.963 | 3.4509 | 29.7692 | 26.0171 | 141.461 | 8.6738 | 260.008 | 0 | 0.00022367 | 0.22001 | 0.16107 | 0.16107 | 39.3055 | 8.497 | 472.125 | 156.254
InterCore | 1
InterKernel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 30.6991 | 0 | 0 | 11.4194 | 0 | 0 | 54.5261 | 0 | 0 | 0 | 0 | 0 | 10.9279 | 0 | 0 | 18.7623 | 0 | 0 | 0 | 0 | 0 | 2.4945 | 0 | 67.7813 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.22266 | 0 | 0 | 0 | 0 | 0.076902 | 0 | 0 | 5.9505 | 0 | 0 | 0 | 0 | 0 | 2.4229 | 0
#REF! | 1
Misses | 513.283 | 1005.22 | 513.436 | 589.945 | 140.628 | 315.642 | 504.652 | 334.911 | 51.1432 | 484.424 | 63.5241 | 159.929 | 111.968 | 43.975 | 20.7328 | 11.3278 | 3.4865 | 3.4865 | 197.683 | 347.417 | 320.846 | 32.4849
IntraWarp | 0 | 0 | 0 | 0 | 0 | 0 | 129.8 | 0.50966 | 0 | 576.307 | 1403.72 | 6.3562 | 302.635 | 61.7589 | 221.885 | 390.144 | 0.19534 | 0.1 | 2857.97 | 241.89 | 953.205 | 5401.53
IntraBlock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 53.1284 | 12.2653 | 119.771 | 302.576 | 31.8466 | 117.453 | 0.20961 | 0 | 1.0139 | 0.0035407 | 0 | 0 | 238.178 | 1510.06 | 2.6914
IntraCore | 0 | 0 | 0 | 0 | 0.0013581 | 0.085754 | 2.9763 | 0.52715 | 0.41182 | 9.1497 | 3.4591 | 0.29971 | 19.7011 | 0 | 0.00022367 | 0.087704 | 0.0030731 | 0 | 0 | 8.4433 | 224.899 | 83.0307
#REF! | 1
InterKernel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.062925 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.60514 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
IntraWarp | 0.0027375 | 0.038346 | 0 | 0 | 3.6529 | 0 | 0.62314 | 100.972 | 9.8869 | 238.9932 | 712.4064 | 6.9657 | 477.8646 | 1500.75 | 1657.7974 | 1495.4789 | 378.561 | 245.678 | 1235.9278 | 11.7198 | 32.346 | 11.1193
IntraBlock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.37561 | 619.8006 | 595.034 | 653.861 | 115.086 | 292.9672 | 44.1431 | 0.030643 | 1.7089 | 8.3804 | 0.09006 | 0.25239 | 102.6144 | 14.8266 | 1.4429
IntraCore | 0 | 0 | 0 | 0 | 0.017429 | 23.2576 | 9.9868 | 9.0556 | 71.4455 | 22.1536 | 140.224 | 8.6273 | 250.806 | 13.0167 | 0 | 0.22001 | 0.16107 | 0.00035043 | 0.12871 | 0.70228 | 241.559 | 73.9879
InterCore | 0.11497 | 0.53684 | 0.11501 | 0.014411 | 7.487 | 295.8344 | 243.9861 | 304.779 | 60.6075 | 347.551 | 59.2645 | 1.0849 | 60.1884 | 3.9515 | 0.037801 | 0.04234 | 1.2759 | 0.03662 | 0.076261 | 40.5412 | 181.8848 | 32.285
InterKernel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 566.675 | 0 | 0 | 118.5381 | 0 | 0 | 37.2186 | 0 | 0 | 130.423 | 0 | 0 | 120.618 | 0 | 0 | 9.5382 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 78.0039 | 0 | 85.2694 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.7593 | 0 | 0 | 0 | 1.6955 | 0 | 0 | 73.3434 | 0 | 0 | 0 | 0 | 0 | 0.82854 | 0
#REF! | 1
Misses | 513.2914 | 1005.2486 | 513.4439 | 53.97 | 30.1685 | 37.2259 | 130.4351 | 120.632 | 4.7732 | 136.8849 | 4.2713 | 82.2772 | 32.9572 | 44.0134 | 18.2681 | 5.7601 | 2.2137 | 8.035 | 0.0053473 | 142.6386 | 109.1385 | 1.845
IntraWarp | 0 | 0 | 0 | 0 | 0.093936 | 0 | 0.62313 | 97.88 | 9.8529 | 238.993 | 712.3944 | 6.8826 | 473.7863 | 1159 | 1332.7139 | 1486.05 | 262.976 | 18.7358 | 1090.3984 | 11.7198 | 32.3424 | 11.1193
IntraBlock | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.37546 | 506.6175 | 595.034 | 597.911 | 31.639 | 291.871 | 43.5257 | 0 | 1.7087 | 0.68469 | 0.067808 | 0.1914 | 102.6144 | 14.8266 | 1.4429
IntraCore | 0 | 0 | 0 | 0 | 0.016976 | 23.2576 | 5.7416 | 8.628 | 49.5959 | 22.1536 | 108.533 | 2.7185 | 250.5227 | 12.722 | 0 | 0.22001 | 0.13281 | 0 | 0.062376 | 0.70228 | 220.578 | 73.9879
InterCore | 0.11497 | 0.53684 | 0.11501 | 0.014411 | 5.6687 | 295.8344 | 210.5369 | 301.907 | 13.1178 | 347.551 | 51.8748 | 1.0401 | 59.6183 | 3.5603 | 0.03713 | 0.04234 | 0.19126 | 0.029611 | 0.054793 | 40.5412 | 41.9494 | 32.285
InterKernel | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.4111 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00015337 | 0 | 0 | 0.0072708 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 22.53 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0088838 | 0 | 0 | 0 | 0.026168 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.47168
Left bar Unbounded Cache, Right bar Bounded Cache
L1/L2 Streaming Applications
L1 Streaming
Inter-warp conflict
contention
Cache
Friendly
Applications
L1 Cache
L2 Cache
Unbounded L1
Bounded L1
Unbou L2
Bound L2
Per Kilo Cycles
Per Kilo Cycles
Inter-warp Thrashing
Intra-warp
Conflict Contention
+Thrashing
Notes: L1 16KB +LRU + GTO scheduler
L2 786 KB + LRU
L1: Write back local, Write-evict Global, no-write allocate
L2 Write back with write allocate
Unbounded L2 is measured while L1 is bounded (=16 KB GTO)
Notes:
1- Global Read after Read locality is only exploited in L1
2- Read after Write, Write after Write, Write after Read, Read after Write after Read are all exploited in L2

## Slide 17: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 18: Idea#1: Dynamically Bypassing Streaming Applications
Every N cycles
  If Miss rate of L1 cache sets > Threshold
    Disable L1 Cache (i.e. bypassing all the memory accesses)
  Else
    Enable L1 Cache
The same for L2 cache.
During bypassing, the cache controller is enabled and tags are updated to compute the new miss rate.

## Slide 19: Static Warp Throttling Effect on BFS
Chart: 
IPC | 14.9244 | 25.294 | 32.51 | 33.9491 | 34.0193 | 33.2906 | 32.8493 | 31.8703 | 31.4496 | 30.9774 | 30.823 | 30.5442 | 30.5413 | 30.2558 | 30.3659 | 30.3234 | 30.3344 | 30.2493 | 30.2784 | 30.2248 | 30.1606 | 30.2898 | 30.1627 | 30.2756
MPKI | 23.9212 | 25.0372 | 27.1464 | 29.6098 | 31.9835 | 34.014 | 35.6579 | 36.7399 | 37.6549 | 38.262 | 38.7108 | 39.0351 | 39.2601 | 39.4708 | 39.5411 | 39.634 | 39.6807 | 39.6248 | 39.6645 | 39.6584 | 39.6824 | 39.6066 | 39.6142 | 39.6327
IPC
MPKI
Maximum TLP
Lowest MPKI
Maximum IPC
#Active Warps

## Slide 20: Idea#2: Dynamic Warp Throttling Via Cores Sampling (DWT-CS)
Every N cycles
  If MPKI of L1 cache sets > Threshold
  Cores Sampling for M Cycles
More Details in paper
Core1
Core2
Core3
Core4
Core5
1 warp
2 warps
3 warps
4 warps
5 warps
#Instruction
#Instruction
Find the winner core and propagate the value to the other cores
    The cores throttle the number of active warps to the new propagated value

## Slide 21: Alleviating Cache Conflicts
Recent works proposed cache bypassing on associativity stalls.
  Jia et al. “MRPB: Memory Request Prioritization for Massively Parallel Processors”, HPCA 2014.
Cache Bypassing is not an effective method to deal with GPU associativity problem.
In many cases, bypassing occurs while the other cache sets are underutilized.

## Slide 22: Cache-bypassing-on-stalls Shortcomings
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Memory-coalescing
Warp Threads memory loads
Indexer
L1 Cache

## Slide 23: Cache-bypassing-on-stalls Shortcomings
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Memory-coalescing
Indexer
L1 Cache
1- Other cache sets are Underutilized
Idea: Improve the
Indexer Function instead
2- Over the next loop iterations, the first four threads and the second four threads evict the lines of each other causing severe conflict misses

## Slide 24: Idea# 3: Employing Pseudo Random Interleaving Caches (PRIC)
In this work, instead of bypassing, we employ a better cache indexing function, Pseudo Random Interleaving Caches (PRIC)
  Rau, B. Ramakrishna. "Pseudo-randomly interleaved memory" MICRO 1991
  Based on polynomial modulus mapping.
  Near-randomly and fairly distributes memory requests over cache sets.
  Simple Hardware: 2-3 levels of Xor-ing gates.

## Slide 25: Sequential Interleaving vs PRIC

## Slide 26: PRIC
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
Memory-coalescing
Warp Threads memory loads
Indexer
L1 Cache

## Slide 27: PRIC
Memory-coalescing
Indexer
Set0
Set1
Set2
Set3
Set4
Set5
Set6
Set7
L1 Cache

## Slide 28: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 29: Performance Improvement over Baseline
Chart: 
| BLK | Sprod | VAdd | FWT | NW | HS | CONV | SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV | PEst | B+tree | BP | NN | HMEAN_st | HMEAN_con | HMEAN
Column2 | 1.0694 | 1.371 | 1.7768 | 1.0081 | 1.4787 | 1.4883 | 1.1557 | 2.6016 | 1.2474 | 2.8997 | 2.0688 | 2.0612 | 1.06 | 1.946 | 1.9192 | 5.0999 | 21.1201 | 16.8776 | 1.0042 | 0.99788 | 1.0017 | 0.99513 | 1.2885 | 2.301 | 1.5477
Normalized IPC
6.1
21.1
16.8
1.3
2.3
1.5
No loss

## Slide 30: Miss rate Reduction
Chart: Miss rate %
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV
Baseline | 88.321 | 98.1831 | 65.5287 | 47.8697 | 88.1182 | 73.0064 | 96.5161 | 82.1001 | 79.4104 | 99.9468 | 99.7494
DWT+PRIC | 74.9775 | 13.3613 | 24.4813 | 17.958 | 67.3653 | 69.5602 | 49.7114 | 26.5118 | 3.9056 | 11.7074 | 18.6857
Unbounded | 72.2129 | 7.33 | 23.6785 | 1.9368 | 49.2936 | 7.9078 | 3.1406 | 1.0572 | 0.6015 | 0.6315 | 7.7603
More than 80% reduction

## Slide 31: Miss rate Reduction
Chart: Miss rate %
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV
Baseline | 88.321 | 98.1831 | 65.5287 | 47.8697 | 88.1182 | 73.0064 | 96.5161 | 82.1001 | 79.4104 | 99.9468 | 99.7494
DWT+PRIC | 74.9775 | 13.3613 | 24.4813 | 17.958 | 67.3653 | 69.5602 | 49.7114 | 26.5118 | 3.9056 | 11.7074 | 18.6857
Unbounded | 72.2129 | 7.33 | 23.6785 | 1.9368 | 49.2936 | 7.9078 | 3.1406 | 1.0572 | 0.6015 | 0.6315 | 7.7603
More than 60% reduction

## Slide 32: Miss rate Reduction
Chart: Miss rate %
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV
Baseline | 88.321 | 98.1831 | 65.5287 | 47.8697 | 88.1182 | 73.0064 | 96.5161 | 82.1001 | 79.4104 | 99.9468 | 99.7494
DWT+PRIC | 74.9775 | 13.3613 | 24.4813 | 17.958 | 67.3653 | 69.5602 | 49.7114 | 26.5118 | 3.9056 | 11.7074 | 18.6857
Unbounded | 72.2129 | 7.33 | 23.6785 | 1.9368 | 49.2936 | 7.9078 | 3.1406 | 1.0572 | 0.6015 | 0.6315 | 7.7603
Nearly achieves the same miss rate of unbounded cache

## Slide 33: Related Work
Cache-Conscious Wavefront Scheduling (CCWS) [Micro 2012]
  Addresses thrashing problem only
Memory Request Prioritization Buffer (MRPB) [HPCA 2014]
  Addresses thrashing and conflict problems.
  Bypassing on associativity stalls.
  Reorder prioritization buffer is used, so that requests from the same warp are grouped and sent to the cache together.
More Related Works in the paper

## Slide 34: Compared to CCWS and MRPB
Chart: Normalized IPC
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV | HMEAN
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CCWS | 1.0006 | 0.99857 | 0.99878 | 0.66108 | 0.9804 | 1.118 | 2.1106 | 1.6007 | 4.9059 | 1.0026 | 1 | 1.1307
MRPB | 2.0501 | 1.233 | 1.656 | 1 | 1.6483 | 1.1085 | 1.7964 | 1.572 | 2.0984 | 5.2152 | 4.2116 | 1.6897
DWT-PRIC | 2.6016 | 1.2474 | 2.8997 | 2.0688 | 2.0612 | 1.06 | 1.946 | 1.9192 | 6.12 | 21.1201 | 16.8776 | 2.3169
2.1X and 1.3X over CCWS and
MRPB respectively
1.06X and 1.3X
16X and 5X
DWT-PRIC outperforms CCWS and MRPB by a harmonic mean 1.7X and 1.4X respectively
Steady
Thrashing
Non-Steady
Thrashing
They benefit from both PRIC and DWT-CS

## Slide 35: PRIC vs High Associativity
4way+PRIC is able to achieve 97% of fully-associative cache's performance
Chart: Normalized IPC
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | SYRK | GESUMMV | HMEAN
4-way | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
16-way | 2.3882 | 1.247 | 2.8565 | 1.1246 | 1.4588 | 3.3768 | 1.4846 | 1.701
32-way | 2.5903 | 1.247 | 2.906 | 1.3461 | 1.7394 | 6.0838 | 1.8641 | 1.9714
64-way | 2.5911 | 1.2459 | 2.9078 | 2.0516 | 1.8528 | 21.04 | 2.2 | 2.2863
4-way+PRIC | 2.6016 | 1.2474 | 2.8997 | 2.0688 | 2.0612 | 21.1201 | 19.48 | 2.6943
Fully-Assoc | 2.6089 | 1.2449 | 2.9032 | 2.1789 | 2.075 | 23.0751 | 19.9831 | 2.7288
4way+PRIC outperforms 64-way cache by 1.16X while requiring simple hardware

## Slide 36: Outline
Motivation
Problem Definition
Experimental Setup
Workload Characterization
Proposed Methods
Experimental Results
Conclusion and Future Work

## Slide 37: Conclusions
We propose a low-cost thrashing-resistant conflict-avoiding streaming-aware GPGPU cache management scheme.
  It dynamically detects and bypasses streaming applications.
  Dynamic Warp Throttling via Cores Sampling (DWT-CS) is proposed to alleviate cache thrashing.
  We employ a better cache indexing function, Pseudo Random Interleaving Cache (PRIC), to mitigate associativity stalls and eliminate conflict misses.
Our proposed method improves the average performance of streaming and contention applications by 1.2X and 2.3X respectively.
PRIC is able to outperform bypassing-on-stalls approach and high associativity caches.

## Slide 38: Future Work (I): Fine-Grained Bypassing Mechanism
Chart: Miss rate %
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV
Baseline | 88.321 | 98.1831 | 65.5287 | 47.8697 | 88.1182 | 73.0064 | 96.5161 | 82.1001 | 79.4104 | 99.9468 | 99.7494
DWT+PRIC | 74.9775 | 13.3613 | 24.4813 | 17.958 | 67.3653 | 69.5602 | 49.7114 | 26.5118 | 3.9056 | 11.7074 | 18.6857
Unbounded | 72.2129 | 7.33 | 23.6785 | 1.9368 | 49.2936 | 7.9078 | 3.1406 | 1.0572 | 0.6015 | 0.6315 | 7.7603

## Slide 39: Future Work (II): Resistant to Unstable Thrashing
Chart: Miss rate %
| SRAD | 3DS | 2DCONV | MM | SCLUSTER | BFS | SPMV_S | IIX | KM | SYRK | GESUMMV
Baseline | 88.321 | 98.1831 | 65.5287 | 47.8697 | 88.1182 | 73.0064 | 96.5161 | 82.1001 | 79.4104 | 99.9468 | 99.7494
DWT+PRIC | 74.9775 | 13.3613 | 24.4813 | 17.958 | 67.3653 | 69.5602 | 49.7114 | 26.5118 | 3.9056 | 11.7074 | 18.6857
Unbounded | 72.2129 | 7.33 | 23.6785 | 1.9368 | 49.2936 | 7.9078 | 3.1406 | 1.0572 | 0.6015 | 0.6315 | 7.7603

## Slide 40: Thanks!